## Slide 1: A-Course Controls Assignment “Controlling in the Wind” Photon Toolchain
Dave Gutz
April 2017

## Slide 2: Summary
This installs utilities and drivers to compile Photon firmware and applications completely offline. It appears to not interfere with the normal particle cli process.

## Slide 3: Step 0: Install link shell extension (LSE)
Link to download:
http://download.cnet.com/Link-Shell-Extension-64-bit/3000-2248_4-75213087.html
Link to manual:
http://www.howtogeek.com/howto/16226/complete-guide-to-symbolic-links-symlinks-on-windows-or-linux/
Click here. It will make you restart explorer.
Makes it easy to modify Arduino code

## Slide 4: Reference Guide
https://learn.sparkfun.com/tutorials/photon-development-guide/all
The following pages step through the setup of this offline process
Scroll down to ARM GCC and DFU Bootloader (Offline) for reference....

## Slide 5: Step 1: Install GNU Tools for ARM
Link to download:
https://launchpad.net/gcc-arm-embedded
Click “Windows installer for admin install”
Needed to compile Photon
Click “Add path to environment variable”
Close this window by “X” ing it.

## Slide 6: Step 2: Install Make for Windows
Click “Setup” to download make-3.81.exe. Run as admin. Full installation, all defaults.
Successful install will finish without any notifications
Needed to connect compiler to code
http://gnuwin32.sourceforge.net/packages/make.htm

## Slide 7: Step 3: Install dfu-util
Needed to talk to Photon
Click “releases”
Click “dfu-util-0.9-win64.zip”
?? Not sure this was even unzipped on laptop ??
http://dfu-util.sourceforge.net/

## Slide 8: Step 4: Install MinGW
Windows Command Line Tools
https://community.particle.io/t/toolchain-windows/11635
Click “mingw” link
Click “download” for mingw-get-setup.exe. Open; all defaults.
Mark these 4 for installation.
Installation-Apply Changes
Then quit

## Slide 9: Step 5: Modify Path in System Environment Variables
Windows Command Line Tools
C:\Program Files (x86)\GNU Tools ARM Embedded\4.9 2015q1\bin;C:\MinGW;C:\Program Files (x86)\GnuWin32\bin;C:\MinGW\msys\1.0\bin
C:\Program Files (x86)\CVSNT\;C:\Users\210023782\AppData\Local\particle\bin;C:\Users\210023782\AppData\Local\particledev\bin;C:\Program Files (x86)\Microsoft VS Code\bin;C:\Program Files (x86)\GNU Tools ARM Embedded\5.4 2016q3\bin;C:\Program Files (x86)\GnuWin32\bin;C:\MinGW\msys\1.0\bin;C:\Git\bin
On win10 (SEE NEXT PAGE)
C:\Particle\Tools\Git\bin
Latest:
original:

## Slide 10: Windows 10 PATH
C:\Program Files (x86)\GNU Tools ARM Embedded\5.4 2016q3\bin C:\Users\Dave\AppData\Local\particle\bin C:\Users\Dave\AppData\Roaming\npm C:\Particle\Toolchain\Make\bin C:\Particle\Toolchain\MinGW C:\Particle\Toolchain\MinGW\msys\1.0\bin C:\Particle\Toolchain\GCC-ARM\bin C:\Particle\Tools\DFU-util C:\dfu-util-0.8-binaries\win32-mingw32 C:\Users\Dave\AppData\Local\Microsoft\WindowsApps C:\Program Files (x86)\Microsoft VS Code\bin C:\Users\Dave\AppData\Local\atom\bin C:\Program Files (x86)\GnuWin32\bin C:\MinGW\msys\1.0\bin C:\Particle\Tools\Git\bin

## Slide 11: Step 6: Install Particle Firmware
https://github.com/spark/firmware
Get the latest
Click “Download ZIP”
Extract to GitHub Folder
If cloning get latest “release”
I got branch: “release/v0.6.2”
Xxx
“develop”

## Slide 12: Step 7: Install CoolTerm USB
Link to install: http://freeware.the-meiers.org/CoolTerm_Win.zip
Unzip and copy “CoolTerm_0.stc” in this folder to the desktop for easy starting of USB

## Slide 13: Step 8: Make Firmware
- Open cmd.exe as Administrator:
cd “Users\210023782\Documents\GitHub\firmware\main”
Or
cd “C:\Users\<name>\Documents\GitHub\firmware-develop\main” #for Win10
make clean all v=1
***If command not found, PATH not correct. Correct and restart cmd.exe
- Make will complain about “git not found” but will compile anyway.
- This takes about 10 minutes, 2 minutes in Win 10 with a SSD.
***The following message means you did not clone the latest release. Go back to the Install Particle Firmware step.

## Slide 14: FAQ
***This message means you installed wrong version of firmware from github

## Slide 15: Step 9: Install myWindCode
Using Windows Explorer copy myWindCode folder to GitHub\firmware\user\applications
  You could use Link Shell Extension to link the folder
right click on GitHub\Wind\myWindCode
pick link source
browse to GitHub\firmware\user\applications
drop as symbolic link
If needed, using your favorite editor, add the line:
#include <Particle.h>
after the line #include “application.h”
The application must have suffix “.cpp” e.g. myWindCode.cpp

## Slide 16: Redo Loop
Super Clean Redo Loop
Get the newest firmware from origin/develop using GitHub
go into the modules folder, and run w/ the Photon in dfu mode
make clean all program-dfu PLATFORM=photon
The two system firmwares will be updated, and then the user firmware. Will complain about git.
Modify user\src\application.cpp for your code
Go into the main folder, and run stuff above
cd ..\main
make PLATFORM=photon APP=blink program-dfu
With photon in dfu mode go to main folder using cmd as administrator
cd ../../Users/210023782/Documents/GitHub/firmware/main
cd ../../Users/Dave/Documents/GitHub/firmware/main
make all PLATFORM=photon APP=myWindCode
make PLATFORM=photon APP=myWindCode program-dfu
dfu-util -d 2b04:d006 -a 0 -i 0 -s 0x80A0000:leave -D ../build/target/user-part/platform-6-m/myWindCode.bin
--or--
make all program-dfu PLATFORM=photon APP=myWindCode